## Slide 1
Evaluation Of Land And Water Resource Management For Pantaron Range, Mindanao
JOSHUA S. DE LEON MSE–Land and Water Resources Engineering and Technology

## Slide 2
OUTLINE
OUTLINE
The management problem and research gap
Objectives and significance
Land-resource assessment
Water-resource assessment
Management-response evaluation
Validation, integration, and expected outputs

## Slide 3
THE MANAGEMENT PROBLEM
CHAPTER 1
Pantaron evidence is dispersed across forest, land, watershed, governance, and downstream basin sources.
Reported pressures differ in date and geographic scope; they are not measured range-wide conditions.
Remote sensing can evaluate resource condition—but not management practice or effectiveness by itself.
A common catchment framework is needed to connect upstream land condition, water pathways, and management action.

## Slide 4
RESEARCH QUESTION
CHAPTER 1
What land and water resource conditions occur in selected Pantaron-linked catchments?
Which pressures and risks are supported by spatial or field evidence?
What management responses are documented, where, and with what implementation evidence?
Which areas need protection, restoration, sustainable land management, monitoring, or further hydrologic investigation?

## Slide 5
OBJECTIVES
CHAPTER 1
1 Delineate selected management catchments and relate them to a verified Pantaron boundary.
2 Evaluate land cover/forest condition, terrain, riparian cover, and erosion susceptibility.
3 Evaluate rainfall, drainage, surface-water occurrence, and targeted field water conditions.
4 Inventory and map documented management responses and governance arrangements.
5 Classify management needs using transparent rules, evidence strength, and uncertainty.

## Slide 6
CONCEPTUAL FRAMEWORK
CHAPTER 2
DRIVERS/PRESSURES • reported and verified land/water pressures
STATE • land cover, forest configuration, terrain, riparian condition, rainfall, drainage, surface water
RESPONSE • protection, restoration, conservation, monitoring, water management, governance
EVALUATION • independent validation, sensitivity, evidence strength, and management-need classification

## Slide 7
LAND-RESOURCE ASSESSMENT
CHAPTER 3
Sentinel-2 L2A seasonal composites with cloud, shadow, invalid-pixel, and terrain-effect checks.
Validated land-cover classes; comparable change only when both periods have adequate reference evidence.
Forest patch, edge/core, and riparian-cover metrics at defensible analysis scales.
Slope and terrain constraints; erosion susceptibility as the core output.
RUSLE only if R, K, LS, C, P inputs and validation are defensible—otherwise no soil-loss-rate claim.

## Slide 8
WATER-RESOURCE ASSESSMENT
CHAPTER 3
Conditioned DEM, verified outlets, complete catchments, and threshold-tested drainage.
CHIRPS v3 rainfall totals, seasonality, anomalies, and dry spells at native 0.05° support.
Surface-water occurrence only where observation density and mixed pixels permit.
Targeted field measurements: stream geometry/flow and calibrated temperature, pH, EC, DO, turbidity where feasible.
Single visits are snapshots—not dependable supply, long-term quality, or regulatory compliance.

## Slide 9
MANAGEMENT-RESPONSE EVALUATION
CHAPTER 3
Review plans, legal instruments, agency projects, restoration records, monitoring reports, and authorized local evidence.
Record responsible institution, location, period, intended outcome, implementation evidence, and monitoring indicator.
Distinguish planned, implemented, monitored, and evaluated actions.
Claim effectiveness only with intervention exposure, timing, outcome evidence, and a defensible comparison.
Interviews require adviser approval, ethics clearance, permission, and protection of sensitive knowledge.

## Slide 10
SAMPLING AND VALIDATION
CHAPTER 3
Select 2–4 catchments by Pantaron relationship, management relevance, contrast, data completeness, and access.
Use independent stratified probability samples for land-cover accuracy; separate training, tuning, and evaluation.
Target field sites toward uncertain classes, riparian condition, erosion indicators, and accessible streams.
Record coordinates, time, photos, observer confidence, calibration, recent weather, and access limitations.
Report confusion matrix, class accuracy, area uncertainty, and parameter sensitivity.

## Slide 11
INTEGRATION FOR MANAGEMENT
CHAPTER 3
Compare catchments using land condition, water condition, pressure, and response evidence.
Apply explicit decision rules—never an unexplained weighted suitability score.
Assign needs: PROTECT • RESTORE • SUSTAINABLE LAND MANAGEMENT • MONITOR • INVESTIGATE.
Test alternative buffers, thresholds, class errors, outlet positions, and rainfall support.
Attach evidence strength and limitations to every mapped recommendation.

## Slide 12
EXPECTED OUTPUTS
OUTPUTS
Verified Pantaron-reference and management-catchment map.
Land-cover/forest, terrain, riparian, and erosion-susceptibility outputs.
Rainfall, drainage, surface-water, and field-observation summaries.
Management-intervention inventory and spatial coverage map.
Catchment management-needs matrix with uncertainty and responsible planning use.

## Slide 13
CRITICAL ITEMS TO COMPLETE
GAPS
Authoritative Pantaron boundary, outlets, and selected catchments.
Comparable imagery periods, class scheme, and validation sample-size calculation.
Hydrography, rainfall gauges, field access, instruments, permissions, and safety plan.
Official management plans/intervention records and research-ethics determination.
Primary references for accuracy-adjusted area, landscape metrics, erosion susceptibility, field water QA/QC, and evaluation design.

## Slide 14
THE CONTRIBUTION
A defensible evaluation connecting land condition, water condition, management response, and uncertainty within selected Pantaron-linked catchments.